## Slide 1: Toward Software-Defined Middlebox Networking
Aaron Gember, Prathmesh Prabhu, Zainab Ghadiyali, Aditya Akella
University of Wisconsin-Madison

## Slide 2: Why Middleboxes?
Network
Physical
Data Link
Transport
Session
Presentation
Application
Enterprises heavily rely on middleboxes
[Sherry et al., SIGCOMM 2012]
Network
Data Link
SDN
Transport
Session
Presentation
Application
???
Notes: SDN told us how to provide flexible layer 2 & 3 networking. How do we provide the same flexibility in layers 4-7?

## Slide 3: Middlebox Deployment Models
Arbitrary middlebox placement
New forms of middlebox deployment (VMs, ETTM [NSDI 2011], CoMB [NSDI 2012])
Notes: We are witnessing new models of middlebox deployment within the context of data centers.

## Slide 4: Live Data Center Migration
Move between software-defined data centers
Existing VM and network migration methods
  Unsuitable for changing underlying substrate
Data Center A
Data Center B
  Programmatic control over middlebox state
Notes: Software-defined data center means the details are abstracted away and control of compute, network, and storage has been pushed to layers of software.
You’ll hear about LIve Migration of an Entire network at the end of this session.

## Slide 5: Middlebox Scaling
Add or remove middlebox VMs based on load
Clone VM (logic, policy, and internal state)
  Unsuitable for scaling down or some scaling up
  Fine-grained control
Notes: One solution you may be thinking about is to simply clone the VM. These mechanism is in fact sufficient in some cases.

## Slide 6: Our Contributions
Classify middlebox state, and discuss what should be controlled
Abstractions and interfaces
  Representing state
  Manipulating where state resides
  Announcing state-related events
Control logic design sketches
Notes: So to work towards meeting these requirements and enabling these rich scenarios, our work makes the following contributions.

## Slide 7: Software-Defined Middlebox Networking
Controller
Middlebox
App
App
Middlebox
SDN-like Middleboxes
IPS
Today
Notes: To meet these requirements and enable these scenarios, we advocate for software-defined middlebox networking. To understand exactly what we mean by this, let’s first take at look at how a middlebox works today.

## Slide 8: Key Issues
Controller
Middlebox
How is the logic divided?
Where is state manipulated?
What interfaces are exposed?
App
App
Middlebox
Notes: Vendors would expose these interfaces on middleboxes, just as switch vendors expose OpenFlow interfaces today. In fact, a specific cloud provider might offer middleboxes-as-a-service and only offer middleboxes from vendors that implement these interfaces.

## Slide 9: Middlebox State
Configuration input
State: ESTAB Seq #: 3423
Server: B
CPU: 50%
Hash: 34225
Content: ABCDE
  Significant state diversity
+ detailed internal records
Balance Method:
Round Robin
Cache size: 100
Src: HostA
Server: B
Proto: TCP
Port: 22

## Slide 10: Classification of State
Balance Method:
Round Robin
Cache size: 100
Src: HostA
Server: B
Proto: TCP
Port: 22
State: ESTAB Seq #: 3423
Server: B
CPU: 50%
Hash: 34225
Content: ABCDE
Action
Supporting
Tuning
Internal & dynamic
Many forms
Only affects performance, not correctness

## Slide 11: How to Represent State?
Policy
Language
Src: HostA
Server: B
Proto: TCP
Port: 22
State: ESTAB Seq #: 3423
Server: B
CPU: 50%
Hash: 34225
Content: ABCDE
  Unknown structure
  Significant diversity
  May be shared
Per flow
Shared
  Commonality among middlebox operations
1000101
1101010
0101001
1111000
1010110

## Slide 12: State Representation
Key: protocol header field/value pairs identify traffic subsets to which state applies
Action: transformation function to change parts of packet to new constants
Supporting: binary blob
Key
Action
Supporting
Binary Blob
Field1 = Value1
…
FieldN = ValueN
Offset1 → Const1
…
OffsetN → ConstN
Only suitable for per-flow state
Not fully vendor independent

## Slide 13: How to Manipulate State?
Controller
Middlebox
Today: only control some state
  Constrains flexibility and sophistication
Manipulate all state at controller
  Removes too much functionality from middleboxes
Notes: A natural way to provide control over state would be to perform all state manipulation at the controller.
SDN makes switches dumb; doesn’t work for MBs.

## Slide 14: State Manipulation
Control over state placement
  Broad operations interface
  Expose state-related events
Controller
IPS 1
IPS 2
Create and
update state
Determine where state resides

## Slide 15: Operations Interface
Action
*
Key
SrcIP = 10.10.0.0/16
DPort = 22
Key
SrcIP = 10.10.54.41
DstIP = 10.20.1.23
SPort = 12983
DPort = 22
State = ESTAB
Supporting
get ( , )
Filter
SrcIP = 10.10.54.41
add ( , )
Action
DROP
Key
DstIP = 10.20.1.0/24
Source | Destination | Proto | Other | Action
* | 10.20.1.0/24 | TCP | * | DROP
remove( , )
Filter
…
Need atomic blocks of operations
Potential for invalid manipulations of state
Notes: Addressing the issue of invalid state manipulations is more complex for middleboxes than in SDN. The state in even a single middlebox can be inconsistent.

## Slide 16: Events Interface
Firewall
Triggers
  Created/updated state
  Require state to complete operation
Contents
  Key
  Copy of packet?
  Copy of new state?
Controller
Balance visibility and overhead

## Slide 17: Conclusion
Need fine-grained, centralized control over middlebox state to support rich scenarios
Challenges: state diversity, unknown semantics
get/add/remove ( , )
…
Action
Offset1 → Const1
…
Key
Field1 = Value1
…
Supporting
Binary Blob

## Slide 18: Open Questions
Encoding supporting state/other action state?
Preventing invalid state manipulations?
Exposing events with sufficient detail?
Maintaining operation during state changes?
Designing a variety of control logics?
Providing middlebox fault tolerance?

## Slide 19: Related Work
Simple Middlebox COntrol protocol [RFC 4540]
Modeling middleboxes [IEEE Network 2008]
Stratos – middleboxes in clouds [UW-Madison TR]
ETTM – middleboxes in hypervisors [NSDI 2011]
COnsolidated MiddleBoxes [NSDI 2012]
Efficiently migrating virtual middleboxes [SIGCOMM 2012 Poster]
LIve Migration of Entire network [HotNets 2012]

## Slide 20: Middlebox Scaling
Add or remove middlebox VMs based on load
Clone VM (logic, policy, and internal state)
Move some long-lived flows to balance load
  Unsuitable for scaling down
  Fine-grained control
Notes: One solution you may be thinking about is to simply clone the VM. These mechanism is in fact sufficient in some cases.

## Slide 21: 3) Virtual Server Provisioning
Add VMs with security or performance needs
Modify and/or add to MB policy
  Middlebox-specific configuration interfaces
  Distributed, manual process => high complexity
  Programmatic and centralized control