## Slide 1: Measuring Control Plane Latency in SDN-enabled Switches
Keqiang He, Junaid Khalid, Aaron Gember-Jacobson, Sourav Das, Chaithan Prakash,
Aditya Akella, Li Erran Li and Marina Thottan
Notes: Hello everyone, I am Keqiang He. Today, I am going to present our work on measuring control plane latency in SDN-enabled switches.
This is a collaborated effort of U Wisconsin and Bell Labs.

## Slide 2: Latency in SDN
Centralized Controller
app
app
app
OpenFlow msgs
Some XXX msecs??
Can be as large as 10 secs!!!
Time taken to install 100 rules ?
Data plane
Control plane
Notes: SDN advocates for the separation of control and data planes in network devices, and provides a logically centralized controller to program data plane states.
In SDN, switch rules can be programed in reactive mode and proactive mode using OpenFlow messages.
Now, let’s ask a question -- if we want to install 100 rules into the data plane, how much time it takes?
We may think it should be extremely fast, may be in order of a few msec.
However, we find that the latency for installing these 100 flows can be as large as 10 secs on production SDN switches.

## Slide 3: Do SDN apps care about latency?
Intra-DC Traffic Engineering
MicroTE [CoNEXT’11] routes predictable traffic on short time scales of 1-2 sec
Fast Failover
Reroute the affected flows quickly in face of failures
Longer update time increases congestion and drops
Mobility
SoftCell [CoNEXT’13] advocates SDN in cellular networks
Routes setup must complete within ~30-40 ms
Latency can significantly undermine the effectiveness of many SDN apps
Notes: Why is latency important? Some applications may not. But there are some applications that are extremely sensitive to latencies in order to meet their objectives.
The first example is fine-grained traffic engineering in data centers. For example, MicroTE [CoNEXT2011] needs to route predictable traffic on short time-scales of a 1-2s.
The second example is fast failover: when failures occur, the SDN management application quickly setup new paths for affected flows , while may also rerouting other flows to minimize the extent of congestion and drops.
Finally, recent work like SoftCell advocates to use SDN to simplify path setup in cellular networks. In such setting, paths must be setup within a small latency bound of about 40 msec.
Our study shows that the latency can undermine the effectiveness of SDN apps significantly, please refer our tech report for details.

## Slide 4: Factors contributing to latency?
Speed of Control Programs and Network Latency
Latency in Network Switches
Control Software Design and Distributed Controllers
Not received much attention
Notes: So, what are the factors contributing to latency?
the first is the speed of controller software and network latency. The second is the control plane latency in network switches.
Recent advances in control software design and distributed controller have overcome the first issue to some extent, however, the second issue has not received much attention.

## Slide 5: Our Work
Latency in network switches
Two contributions:
Systematic experiments to quantify control plane latencies in production switches
Factors that affect latency and low level explanations
Notes: The second problem is the main focus of our work.
We make two contributions in this work:
1) We systematically quantify latencies on four production SDN switches
2) We exam various kinds of factors that may affect latency and provide low level explanations for the long latency phenomena

## Slide 6: Elements of Latency – inbound latency
Inbound Latency
PHY
PHY
Switch
Controller
I1: Send to ASIC SDK
I2: Send to OF Agent
I3: Send to Controller
Packet
CPU
Memory
DMA
ASIC SDK
OF Agent
I2
CPU board
Forwarding Engine
Lookup
Hardware Tables
No Match
I1
PCI
Switch Fabric
I3
Notes: We classify the control plane latency into two categories.
The first is inbound latency. When a packet arrives at a switch port, the switch ASIC does a lookup on the hardware table to find a matching entry. If matching entry is found then the packet is forwarded at line rate.
If no matching entry is found, the following sequence of events takes place:
(I1) Switch ASIC decides to send the packet to the switch’s CPU via the PCI/PCIe bus.
(I2) The ASIC SDK gets the packet and dispatches it to the switch-side openflow agent.
(I3) The agent processes the packet, and sends to the controller a packet_in message which includes the packet header.
All of three steps construct the inbound latency.

## Slide 7: Elements of Latency – outbound latency
Outbound Latency
PHY
PHY
Switch
Controller
O1: Parse OF Msg
O2: Software schedules the rule
O3: Reordering of rules in table
O4: Rule is updated in table
Memory
CPU
ASIC SDK
OF Agent
O2
DMA
O1
Forwarding Engine
Lookup
Hardware Tables
PCI
O4
O3
Switch Fabric
CPU board
Notes: The application on the controller sends flow_mod messages to update flow table. The flow_mod message specifies the matching fields and action of a rule and this rule is finally placed in the switch hardware table.
flow_mod processing: When the switch receives a flow_mod, it takes the following steps:
(O1) The OpenFlow agent running on the CPU parses the OpenFlow message.
(O2) The software schedules the rule to be applied to hardware tables, typically TCAM.
(O3) Depending on the nature of the rule, the chip SDK may require existing rules on the switch to be moved around
(O4) The hardware table is updated with the rule
All of four steps construct the outbound latency.

## Slide 8: Measurement Scope
Inbound Latency
  Increases with flow arrival rate
  Increases with interference from outbound msgs
  Higher CPU usage for higher arrival rates
Outbound Latency
  Insertion
  Modification
  Deletion
Please see our paper for details
Notes: We measured both inbound latency and outbound latency.
For inbound latency, please see our paper for detaills.
In this presentation, I mainly focus on the outbound latency, that is the insertion, modification and deletion latency.

## Slide 9: Measurement Methodology
Switch | CPU | RAM | OF Version | Flow table size | Data Plane
Vendor A | 2 Ghz | 2GB | 1.0 | 4096 | 40*10G+4*40
Vendor B-1.0 | 1 Ghz | 1GB | 1.0 | 896 | 14*10G+4*40G
 |  |  | 1.3 | 1792 (ACL) | 
Vendor B-1.3 |  |  |  |  | 
Vendor C | ? | ? | 1.0 | 750 | 48*10G+4*40G
Notes: We carried out our experiments on 4 production switches from 3 vendors as shown in the table on the slide.
We focus on OpenFlow protocol – three of them are running OF1.0, the other one is running OF1.3

## Slide 10: Insertion Latency Measurement
eth0
eth1
eth2
Control Channel
Flows IN
Flows OUT
OpenFlow Switch
SDN
Controller
Pktgen
Libpcap
Pre-install 1 default
“drop all” rule with low priority
1Gbps of 64B Ethernet packets
Insert B rules
in a burst (back-to-back)
t0
t1
Per rule insertion latency
= t1 – t0
Notes: This shows the experiment setup we use. The SDN controller, packet generator and receiver are all located on same machine to get accurate timings. All the timestamps are measured by examining data plane packets except for inbound latency.

## Slide 11: Insertion Latency – Priority Effects
Affected by priority patterns on all the switches we measured
Per rule insertion always takes order of msec
Vendor B-1.0 switch
Vendor A switch
Chart: (a) Burst size 100, same priority
Chart: (b) Burst size 100, incr. priority
Chart: (a) Burst size 800, same priority
Chart: (b) Burst size 800, decr. priority
Notes: We observed that the insertion latency is affected by the priority patterns of rules being inserted on all the 4 switches we measured.
Per rule insertion delay is always in order of msec which is higher than what the state-of-art TCAM can support.
These are the results from vendor B-1.0 switch.
Fig (a) shows the results of experiment when a burst of rules all with same priority was inserted. The avg delay is 3 msec.
For incr priority as shown in fig (b): Avg delay is 9 msec and per rule insertion latency increases with number of rules. The reason is TCAM reordering.
We observed similar trends on Vender A switch
The only difference here is that higher latencies are observed when rules are inserted in decreasing priority order as shown in figure (b). That means this switch stores lower priority rules at low memory addresses. For same and incr priority as shown in figure (a) we see that Ayg delay is 1 msec and per rule insertion delay does not vary with burst size.

## Slide 12: Insertion Latency – Table occupancy Effects
Affected by the types of rules in the table
Vendor B-1.0 switch
Chart: (a) low priority rules into a table with high priority rules
| 10 | 20 | 50 | 100 | 150 | 200 | 300 | 400 | 500 | 600
table 100 | 38.1349 | 50.5421 | 151.7209 | 273.455 | 428.3069 | 568.985 | 879.5979 | 1234.92 | 1605.5689 | 2064.207
table 400 | 36.4361 | 70.5499 | 166.0509 | 315.347 | 501.1549 | 668.473 | 1105.3849
Chart: (b) high priority rules into a table with low priority rules
| 10 | 20 | 50 | 100 | 150 | 200 | 300 | 400 | 500 | 600
table 100 | 182.8309 | 419.0139 | 845.1461 | 1766.3649 | 2655.3219 | 3575.1771 | 5329.0069 | 7206.456 | 9001.5 | 10936.362
table 400 | 604.3241 | 1195.4609 | 3077.9741 | 6132.8229 | 9394.0489 | 13104.504 | 18736.3851
table 100 | 182.8309 | 419.0139 | 845.1461 | 1766.3649 | 2655.3219 | 3575.1771 | 5329.0069 | 7206.456 | 9001.5 | 10936.362
table 400 | 604.3241 | 1195.4609 | 3077.9741 | 6132.8229 | 9394.0489 | 13104.504 | 18736.3851
TCAM Organization, Rule Priority & Table Occupancy
Switch Software Overhead
Notes: Insertion latency is also affected by the table occupancy.
The fig shows the experiments we did on vendor B-1.0 switch.
Fig (a) shows the results for the exp in which we pre-insert high priorty rules and insert burst of low priority rules. The fig (b) shows the results for the exp in which we pre-installed low priority rules and then insert burst of higher priority rules. We vary the table occupancy i.e. the number of pre-installed rules.
Fig (b)’s latency is higher because high priority rules displace all low priority rules that are already in the flow table. So, in this case, higher table occupancy has higher insertion latency.

## Slide 13: Modification Latency Measurement
eth0
eth1
eth2
Control Channel
Flows IN
Flows OUT
OpenFlow Switch
SDN
Controller
Pktgen
Libpcap
Pre-install B dropping rules
1Gbps of 64B Ethernet packets
Modify B rules
in a burst (back-to-back)
t0
t1
Per rule modification latency
= t1 – t0
Notes: Modification latency measurement is that of insertion latency.
The differences are that, at the first step, we pre-install B dropping rules, then we modify those dropping rules in a burst

## Slide 14: Modification Latency
Same as insertion latency on vendor A
2X as insertion latency on vendor B-1.3
Notes: We observe that modification latency is same as insertion latency for vendor A.
But it is 2 times larger than insertion latency on Vender B-1.3.

## Slide 15: Modification Latency
Much higher on vendor B-1.0 and vendor C
Not affected by rule priority but affected by table occupancy
Vendor B-1.0 switch
Chart: (a) 100 rules in the table
Chart: (b) 200 rules in table
Poorly optimized switch software 
Notes: However, modification latency is much higher on Vender B-1.0 and Vender C switch. Modification latency is not affected by rule priority structure but it is affected by table occupancy significantly.
For example, the figures show the result from vendor B-1.0 switch. we see that the avg delay is about 30 ms for B = 100 as shown in fig (a). When size of B is doubled, the latency is doubled as well as shown in fig (b). It also grows linearly with burst size (not shown).
Please note that the per-rule insertion latency is 3 msec. Modification is much larger than insertion latency.
Our conversation with Vender B indicate this is due to poorly optimized switch software.

## Slide 16: Deletion Latency Measurement
eth0
eth1
eth2
Control Channel
Flows IN
Flows OUT
OpenFlow Switch
SDN
Controller
Pktgen
Libpcap
Pre-install B dropping rules
& 1 “pass all” rule with
low priority
1Gbps of 64B Ethernet packets
Delete B rules
in a burst (back-to-back)
t0
t1
Per rule deletion latency
= t1 – t0
Notes: Deletion latency measurement is also similar.
The differences are that, at the first step, we pre-install B dropping rules and 1 “pass all” rule with low priority, then we delete B dropping rules in a burst

## Slide 17: Deletion Latency
Higher than insertion latency for all the switches we measured
Not affected by rule priority but affected by table occupancy
Vendor A switch
Chart: (a) 100 rules in table
Chart: (b) 200 rules in table
Deletion is incurring TCAM Reorganization
Notes: Deletion latency is higher than insertion on all the 4 switches we measured. It is not affected by rule priority but is affected by table occupancy.
For example, the figures show the results from vendor A switch.
We see that per rule deletion delay is directly proportional to the table occupancy and the latency decreases as the table occupancy drops as shown in figure (a) and (b) for S =100 and 200 respectively.
We infer that deletion is incurring some kind of TCAM reorganization.

## Slide 18: Recommendations for SDN app designers
Insert rules in a hardware-friendly order
Consider parallel rule updates if possible
Consider the switch heterogeneity
Avoid explicit rule deletion if timeout can be applied
Notes: Here is out recommendations for SDN application designers
first, insert rules in a hardware-friendly order
Second, consider parallel rule updates if possible
Third, consider switch heterogeneity
Finally, avoid explicit rule deletion if timeouts can be applied.

## Slide 19: Summary
Latency in SDN is critical to many applications
Long latency can undermine many SDN app’s effectiveness greatly
Assumption: Latency is small or constant
Latency is high and variable
  Varies with Platforms, Type of operations, Rule priorities, Table occupancy, Concurrent operations
  Key Factors: TCAM Organization, Switch CPU and inefficient Software Implementation
Need careful design of future switch silicon and software in order to fully utilize the power of SDN!
Notes: To sum up,
We argue that control plane latency is critical to many applications
Previous assumption that control plane latency is small or constant is not true.
We found control plane latency is high and variable. It varies with…
Key factors affect latency are…
Finally, Our findings highlight the need for careful design of future switch silicon and software in order to fully utilize the power of SDN.

## Slide 21: Inbound Latency
Increases with flow arrival rate
CPU Usage is higher for higher flow arrival rates
Flow Arrival Rate (packets/sec) | Mean Delay per packet_in (msec) | CPU Usage
100 | 3.32 | 15.7 %
200 | 8.33 | 26.5 %
vendor A switch
Notes: We observed that the inbound latency increases with flow arrival rate.
For example, on Vender A switch,
when the flow arrival rate is 100 per second, the average packet_in latency is 3 msec, when the rate is increased to 200, the average latency increases to 8 msec.
We also observe that the CPU usage is higher with higher flow arrival rate.

## Slide 22: Inbound Latency
vendor A switch. Flow Arrival Rate = 200/s
Increases with interference from outbound msgs
Chart: (a) with flow_mod/pkt_out
Chart: (b) w/o flow_mod/pkt_out
Low Power CPU
Software Inefficiency
Notes: Further more, we observe that inbound latency increases with interference from concurrent processing of outbound messages such as flow_mod and pkt_out by the switch.
Fig (a) shows the results for experiments in which outbound messages were generated by the controller in response to inbound message. Fig (b) shows the results for the experiment in which the pkt_in was dropped by the controller and no outbound messages were generates in response.
We can see that the inbound delay is quite high and variable when there is interference from outbound messages.
We infer that there are 2 factors contributing to inbound delays:
1)Low-end CPU: Switch CPU is one of the factors responsible for inbound latency since switches utilization is goes high when the packets are generated at very high rate where we also see increased latencies.
2)Software Inefficiency: Interference with flow_mod and packet_out processing also contributes to the inbound latencies which may be because of inefficient handling of inbound and outbound messages by the switch software.

## Slide 23: How accurate?
500 flows
1Gbps
64B Ethernet packet
Inter-packet gap of a flow = 256 us
Solution: Either increase the packet rate or reduce the number of flows or measure the accumulated latency for many flows