## Slide 1: Challenges in Unifying Control of Middlebox Traversals and Functionality
Aaron Gember, Theophilus Benson, Aditya Akella
University of Wisconsin-Madison

## Slide 2: Components of Enterprise Networks
Middleboxes make up 40% of the network devices in large enterprises with over 200K hosts1
Enterprises spent on average over1 million dollars over the last 5 years to acquire middleboxes1
A Survey of Enterprise Middlebox Deployments, Justine Sherry and Sylvia Ratnasamy, 2012

## Slide 3: Importance of Middleboxes
Additional component traffic passes through for examination and/or modification
  Not a connection endpoint
  Not responsible for path selection
Ensure security
Optimize performance
Facilitate remote access

## Slide 4: Deploying Middlebox Topologies
Determine objectives – conceptual
Select middleboxes, and ordering – logical
  Select traffic to examine
Plan wiring and network config – physical
Flow Logger
IDS
HTTP

## Slide 5: Deployment Scenarios
Monitor all paths or specific link
On-path vs. Off-path
Enforcing traversals
  Physical chokepoint: wiring inline
  Logical chokepoints: routing hacks
  Software defined networking (SDN)

## Slide 6: Enforcing Desired Traversals
Brittle networks: choke points
  Single point-of-failure
Limited flexibility
  Unable to differentiate based on traffic type
Difficult to expand
With SDN, still difficult to expand – need control over middlebox to expand

## Slide 7: Configuring Middleboxes
Infrastructure dependence
  Distinct language for each vendor
  Hard to migrate between vendors
Topology dependence
  Tied to servers on path
  prevents mobility of server and middleboxes
67% of the outages are caused by misconfiguration of these middleboxes1
Need unified control over middleboxes and network devices
A Survey of Enterprise Middlebox Deployments, Justine Sherry and Sylvia Ratnasamy, 2012

## Slide 8: Benefits of Unification
Easier to verify middlebox configuration
Easier to migrate between infrastructure
Automation leads to flexibility
  Implement energy saving
  Implement bottleneck detection and scaling

## Slide 9: Centralized Unified Control
Configures physical infrastructure
  Routers + Switches: OpenFlow + NOX
  Middleboxes: ??????
Control Plane
High level Objectives
Physical Infrastructure

## Slide 10: Composing Middlebox Topologies
Operator specifies logical topology
Control plane determines path
Flow Logger
IDS
HTTP

## Slide 11: Assumptions
Middlebox deployments are based on high level objectives
A network of SDN switches
  Programmatic control over network

## Slide 12: Challenges
Abstractions for specifying high level constraints
  Simple yet flexible and powerful
  Oblivious to the separation between middleboxes and routers.
Common middlebox interface
  Extensible – support new middleboxes
  Support for vendor specific functionality
Control Plane
Control Plane

## Slide 13: Strawman for Abstracting Configuration
Basic middlebox functionality
Middleboxes should expose:
  Ways to examine and match packets; e.g., regular-expression on payload, IP headers
  Transformations supported; e.g., encryption
  Way to forward; e.g., SSL tunnel, IP
Examine
Transform
Forward

## Slide 14: Challenges of Considering Underlying Infrastructure
Map constraints to physical infrastructure.
  Configure physical infrastructure
Re-adjust configuration to reflect dynamics
  Network topology, middlebox features, and network load

## Slide 15: Strawman for Considering Underlying Infrastructure
LP that matches constraints to exposed MB functionality
    Minimize latency (# of links) or Minimize resource utilization (# of MBs)
    Subject to high level constraints
  Input to LP
    High level goals
    Functionality supported by Middleboxes
    Network topology

## Slide 16: State-of-the-Art
SDN, Policy-Switch, CloudNaaS
  Flexible interposition of middlebox
  No control over configuration
    Difficult to setup rules for flows without knowledge of middlebox transformations
MIDCOM
  Specify which traffic traverses a middlebox
  Doesn’t support specification of functionality

## Slide 17: Summary
Discussed challenges of deploying middleboxes
  Enforcing traversals
  Configuration management
Described outline for unified control
  Presented advantages and challenges